## Slide 1
Lab-scale bubbling fluidized bed development and oxy-combustion validation
Tzu-Lu Fang,Hsien-Tsung Lin,Guan-Bang Chen,Yei-Chin Chao Chen Ming-Hsun Wu*
Department of Mechanical Engineering, National Cheng Kung University, Taiwan
*Contact email: minghwu@mail.ncku.edu.tw
Conclusion
Introduction
Research method
Fuel property analysis
TG-FTIR analysis
Future work
Biomass combustion diagram and carbon cycle closed loop
Thermochemical route of biomass conversion
Van Krevelen diagram
O2/CO2 Recycle (Oxy-fuel) Combustion Capture
Fuel property analysis
Elemental, proximate, fiber and HHV analysis
Thermogravimetric analysis
FTIR
Define Ti and Tb by intersection method and conversion method, respectively.
A large value of S implies that the fuel have better combustion performance
Experimental Setup
Bubbling fluidized bed
Gas flowmeter and preheater
Gas analyzer
Temperature measurement
Gas condenser
BFB system
Bed material (gravel)
Size: 0.177-0.5 mm
Belong to Group B particle, The bed starts bubbling immediately after reaching Umf
Dense bed
Fuel type | Proximate analysis (wt. % dry basis) |  |  | Elemental analysis (wt. % dry basis) |  |  |  |  | HHV (kcal/kg)
 | VM | FC | Ash | C | H | O | N | S | 
PKS | 79.65 | 14.56 | 5.79 | 49.8 | 6.05 | 42.64 | 0.66 | 0.06 | 4754
Coal | 33.66 | 46.3 | 20.0 | 73.3 | 4.17 | 5.25 | 1.44 | 0.52 | 6730
Palm Kernel shell
PKS oxy-combustion validation in fluidized bed
PKS gasification study
Avoid slagging during operation
Fuel
YH2O=0.206; HHV=3817 kcal/kg (as receive basis)
Pretreatment
Under 103 for 24 hour to get dry basis
Bulk density: 0.587 g/cm3
Real density: 0.673 g/cm3
Crushed and sieved to 35 mesh for TG-FTIR exp.
Interaction of LPG/Air flame with bed meterial
PKS combustion
Preheat
Batch feeding and study
The variation of dense bed temperature and downstream gas emission with time