## Slide 1: CF PE3 W208 Weekly Report
Al_Qin

## Slide 2: Outline
Highlight/Lowlight
  SPC Review Result
  PE3 MOC case status
  CIM System Develop
    CF8 Mark/ACT 雲端系統開發

## Slide 3: SPC Review Result

## Slide 4: CFD Weekly Report
CFD key project - SPC Review Result
  Strengthen SPC management
    Add daily review
      Check all chart (Cpk/Cp/k/OCAP ratio), and highlight abnormal chart
Create SPC function “My report”
How to judge it’s “abnormal”
No. | Item | Highlight
1 | OOC | >10%
2 | K | > 0.1
3 | ∆K | >10%
4 | Cp | < Goal
5 | Cpk | < Goal
To catch “abnormal point”
OOC%
K
Cpk
Cp
1
2
4
5
3
∆K

## Slide 5: CFD Weekly Report
CFD key project - SPC Review Result
  Strengthen SPC management
    PE3 SPC management SOP
      Annual health check/ New chart
      Quarter health check
Review
Create
Trace
Optimal
Healthy check
Healthy check
-By tool check
Create new chart
-2 week check window
-SPEC: 4.5σ,Control:3.5σ
Trace new chart
-One month tracing
-check Sigma/OCAP…
Optimal SPEC
-according 1 month data
Trace chart
-One month tracing
-check Sigma/OCAP…
Review chart
-Daily/ Weekly/ Monthly
If need optimal
Review chart
-Daily/ Weekly/ Monthly
Healthy check
-Control limit~ 3.5σ
Optimal limit
-Past 3 months data

## Slide 6: CFD Weekly Report
CFD key project - SPC Review Result
  SPC Review Result
    Create new chart SOP flow
    New chart status tracing
No. |  | Chart ID |  | Chart Name |  | Status |  | Remark
1 |  | 72647 |  | B-ANG-SAD-2P |  | 2. Trace |  | AD4 contact angle (進點數未滿30個)
2 |  | 72396 |  | B-EBRMPB-2500UM |  | 2. Trace |  | CF8 MP EBR (BCOAT29) (進點數未滿30個)
3 |  | 72754 |  | F-ETROXA-ESC-0620A |  | 2. Trace |  | Vigus O2 ETCH (進點數未滿30個)
4 |  | 59322 |  | F-THKMPEW9-23um |  | 2. Trace |  | SMP008 THK (進點數未滿30個)
5 |  | 59321 |  | F-THKOXIA-1610A |  | 2. Trace |  | CVD THK 1.61K (進點數未滿30個)
6 |  | 59323 |  | F-RIOXIA-1.46 |  | 2. Trace |  | CVD RI 1.61K (進點數未滿30個)
7 |  | 21242 |  | F-ADHOXIA-0000ea |  | 2. Trace |  | 百格刀測試
Review
Create
Trace
Optimal
Create new chart
-2 week check window
-SPEC: 4.5σ,Control:3.5σ
Trace new chart
-One month tracing
-check Sigma/OCAP…
Optimal SPEC
-according 1 month data
Trace chart
-One month tracing
-check Sigma/OCAP…
Review chart
-Daily/ Weekly/ Monthly
If need optimal
1
2
3
4

## Slide 7: CFD Weekly Report
CFD key project - SPC Review Result
  SPC Review Result
    PE3 chart summary
    Off-target chart
No. | Type | Off-target (偏邊) |  | New chart
 |  | PASS | NG | 
1 | ADH | 5 |  | 1
2 | DPA | 27 |  | 
3 | EBR | 4 |  | 1
4 | ETH | 2 |  | 
5 | ETR | 16 | 3 | 1
6 | LEAK | 4 |  | 
7 | RI | 3 |  | 1
8 | THK | 13 |  | 2
9 | WPA | 3 |  | 
10 | ANG |  |  | 1
TTL |  | 76 | 3 | 7
No. |  | Chart ID |  | Chart Name |  | Action
1 |  | 39052 |  | F-ETRRWK-ULVAC |  | Low side tracing
2 |  | 23628 |  | F-ETROXA-ESC-0620A |  | Setting shift control limit (3.5 sigma)
3 |  | 70516 |  | F-ETROXA-ESC-0620A |  | Setting shift control limit (3.5 sigma)

## Slide 8: CFD Weekly Report
CFD key project - SPC Review Result
  SPC Review Result
    W208 chart review

## Slide 9: CFD Weekly Report
CFD key project - SPC Review Result
  MP OCAP ratio
    MP OCAP ratio investigation
      Tighten MP THK monthly OCAP count ≤ 5 ea.
Chart name | OOC count |  |  |  | Root cause
 | 2021 |  |  | 2022 | 
 | 10 | 11 | 12 | 01 | 
F-THKMPDW3-79000A | 0 | 8 | 2 | 1 | FCOAT08 Low side
F-THKMPDW5-79000A | 0 | 2 | 1 | 1 | No abnormal
F-THKMPDW7-79000A | 8 | 2 | 0 | 2 | No abnormal
F-THKMPDWB-79000A | 2 | 5 | 5 | 3 | FCOAT09 U4
TTL | 10 | 17 | 8 | 7 | 
TTL (-abnormal point) | 2 | 4 | 1 | 3 | 
Chart: 
| 10 | 11 | 12 | 1 | 2021 | 2022
F-THKMPDW3-79000A

F-THKMPDW5-79000A
F-THKMPDW7-79000A
F-THKMPDWB-79000A

TTL | 10 | 17 | 8 | 7
Normal | 2 | 4 | 1 | 3
Goal | 5 | 5 | 5 | 5
MP THK | Review | Index | During | SPEC
As is | Each chart | Ratio | Monthly | ≤ 10%
To be | Sum | Count | Monthly | ≤ 5 ea.

## Slide 10: PE3 MOC case status

## Slide 11: CFD Weekly Report
CFD key project - PE3 MOC case status
  Description
    MOC SOP flow
ECCP/FCCB
放線
MOC申請
MOC
預計工程變更
-確認
工程變更內容
-申請
請於放線前申請
-Pre MOC
Case呈報
-ECCP/FCCB
Case呈報
-結案
Status轉為Close
不須走MOC流程
MOC
-Internal MOC確認FCCB/ENG
Status轉為Open
-Post MOC
確認Enhance
確認Check list
-結案
No. | Item | Limit
1 | 調轉速 | RMS設定上下限內
2 | 曝光能量 | 原能量 ± 5%
3 | 正常泡復管 | 已經放線管路
4 | NTO/RTO | -

## Slide 12: CFD Weekly Report
CFD key project - PE3 MOC case status
  Status update
    W208 have 1 MOC case closure
    One new cases expected next week (W209)
PE3 Status | 2022 MOC record |  |  |  |  |  |  |  |  |  |  |  |  |  |  | MOC Close count
 | Jan. |  |  | W206 |  |  | W207 |  |  | W208 (Now) |  |  | W209 |  |  | 
ENG | Pre | Post | Close | Pre | Post | Close | Pre | Post | Close | Pre | Post | Close | Pre | Post | Close | 
彭松崑 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
許綱謚 |  |  | 2 |  |  |  |  |  |  |  |  |  |  |  |  | 2
陳保龍 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
陳建宇 |  |  |  |  |  |  |  |  |  |  |  |  | 1 |  |  | 
莊凱晴 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
侯坤劭 |  |  | 2 |  |  |  |  |  |  |  |  |  |  |  |  | 2
莊延年 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
池韋鋌 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
蔡詠翔 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
楊翔斌 |  | 1 [3/4] | 1 |  | 1 [3/4] |  |  | 1 [3/4] |  |  | 1 [3/4] |  |  |  |  | 1
曾國豪 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
張肯睿 |  |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  | 1
林培舜 |  | 1 [2/8] |  |  | 1 [2/8] |  |  |  | 1 |  |  |  |  |  |  | 1
曾明良 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
林毓婷 |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  | 1
林瑋屏 |  |  |  |  |  |  |  | 1 [2/11] |  |  |  | 1 |  |  |  | 1

## Slide 13: CFD Weekly Report
CFD key project - PE3 MOC case status
  Status update
    W208 MOC case item
Change Date | FCCB / MOC No. | Dept | Tool | Change 詳述 | Change scope | EE | PE | PIE | Pre-meeting |  |  |  | Post-meeting |  |  | status
 |  |  |  |  |  |  |  |  | FCCB | RLS criteria | ENG | Date | Enhance results | Checking list | Date | 
2022/1/19 | PE_MOC_20220119_01 | PE3 | BEXPA14 | Release LS layer at BEXPA14 for back up tool | OV10635/OV10640/OV10642 | - | 楊翔斌 | - | Y | Inline | ADI KLA | 1/25 | ADI KLA | Y | 3/4 | Open
2022/2/7 | PE_MOC_20220207_01 | PE3 | FOVEF05 | Release FOVEF05 MP oven | ALL device MP layer | - | 林瑋屏 | - | Y | Inline | DRY PA PL test OM KLA | 2/8 | OM KLA | Y | 2/11 | Open

## Slide 14
CFD Weekly Report
CFD major event - (MOC) Release FOVEF05 MP OVEN
  Description :
    Purpose : To increase producing capacity
    Tool ID : FOVEF05
    Recipe : 175℃ 兩小時 (04-O1752HR)
  Action :
    2/11 Release FOVEF05 MP OVEN
  Data Collection :
    Offline and Inline data is comparable with STD
  Follow Up :
    Burn in lot inline data is normal, suggest to fully release
Condition | Tool | Offline |  | Inline (Pirun/Burn in) | 
 |  | DryPA (ea.) | Peeling (ea.) | OM | KLA
STD | FOVEF04 | 2 | 0 | OK | OK
Spilt | FOVEF05 | 4 | 0 | OK | OK
Result |  | Data comparable |  | Data comparable | 

## Slide 15: Mark8 Dynamic RMS For Recipe Space

## Slide 16
CFD key project - Mark8 Dynamic RMS For Recipe Space
  格子數不足：
CFD Weekly Report
唉~怎麼格子又滿了?
又要先1.刪掉現有的Recipe
然後2.建立一個新的
讓貨先3.開E-Runcard過貨
貨過完4.又要把Recipe改回去
好容易MO唷!!

## Slide 17
CFD key project - Mark8 Dynamic RMS For Recipe Space
  What’s dynamic RMS :
CFD Weekly Report
35.
36.
41.
42.
滿了!
拜~
43.
雲端
A
B
C
A
A
更多的空間
RBG PR
and different recipe body
B
C
A
A
A
機台上建立每個架構殼
系統會抓取當下的主轉
彈性
空間
43.
20.
27.
46.
10.
16.
31.
4.

## Slide 18
CFD key project - Mark8 Dynamic RMS For Recipe Space
  Case1 : Track in while running (Update fail)
    Condition
      Track in @Unit with wafer
      Different Rotational speed (Same recipe body)
      Same PR
      Same unit
CFD Weekly Report
1800
RPM
2000
RPM
1800
RPM
1800
RPM
Track in
Track in
1800 RPM
Wrong rotational speed
1800 RPM
Load port
Unit

## Slide 19
CFD Weekly Report
2200
RPM
2200
RPM
1800
RPM
2000
RPM
2200
RPM
2200
RPM
Track in
Track in
Wrong rotational speed
1800 RPM
2000 RPM
2200 RPM
CFD key project - Mark8 Dynamic RMS For Recipe Space
  Case2 : Track in while non-running (Overwrite)
    Condition
      Track in @Unit without wafer
      Different recipe (Different Rotational speed)
      Same PR
      Same unit
Track in
Load port
Unit

## Slide 20
Wafer in
CFD key project - Mark8 Dynamic RMS For Recipe Space
  Solution : Constraint function
    Add the function of CJ start/ CJ end
      Track in @Unit with/without wafer
      Different Rotational speed (Same recipe body)
      Same PR
      Same unit
CFD Weekly Report
1800
RPM
2000
RPM
Right rotational speed
Track in
Track in
2000
RPM
1800
RPM
Wafer in
1800 RPM
2000 RPM
Load port
Unit

## Slide 21
CFD key project - Mark8 Dynamic RMS For Recipe Space
  Conclusion
CFD Weekly Report
Summary | Recipe body |  |  | 
 | Same |  | Diff. | 
 | Rotational speed |  | Rotational speed | 
 | Same | Diff. | Same | Diff.
Same PR | Continuous | Continuous Non-Continuous | Continuous | Continuous
Diff. PR | Non-Continuous | Non-Continuous | Non-Continuous | Non-Continuous